  - Product And Company Identification

Product Information. 	Mandate Men’s Deodorant Spray

1.2. Relevant identified use of the substance or mixture and uses advised against

Use and substance /mixture:    Fragranced body spray

1.3. Details of the supplier of the safety data sheet

Company name:     L.E.C. (L`pool) Ltd.,

Alfred Street,

Wavertree,

Liverpool,

L15 4LH

Tel: +44 (0)151 734 1411

Fax: +44(0)151 734 4054

Email: steve@insette.com

1.4. Emergence telephone number

Emergency tel:	 +44(0)151 734 1411

Section 2:Hazards identification

2.1 Classification of the substance or mixture

Classification under CLP:   	 	Danger extremely flammable aerosol

Most important adverse effects: 	Extremely flammable

May cause an allergic skin reaction

2.2 Label elements

Hazard statements:  	H222: Danger: extremely flammable aerosol.

Signal words:		Danger

Hazard pictograms: 	GHS02: Flame,

Hazard Statements: 		H222 Extremely flammable aerosol

Precautionary statements: 	P234 Keep only in original container.

P260 Do not breathe vapour/ spray.

P264 Wash contaminated skin thoroughly after handling.

P280 Wear protective gloves/ protective clothing/ eye protection/ face protection.

P301+P330+P331 IF SWALLOWED: Rinse mouth. Do NOT induce vomiting.

P303+P361+P353 IF ON SKIN (or hair): Take off immediately all contaminated clothing. Rinse skin with water/ shower.

P304+P340 IF INHALED: Remove person to fresh air and keep comfortable for breathing.

P305+P351+P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing.

P310 Immediately call a POISON CENTER/ doctor.

P321 Specific treatment (see medical advice on this label).

P363 Wash contaminated clothing before reuse.

P390 Absorb spillage to prevent material damage.

P501 Dispose of contents/ container in accordance with national regulations..

P410+P412: Protect from sunlight. Do not expose to temperatures

exceeding 50 oC

2.3. Other hazards.

Heating may cause an explosion which may cause a fire. Risk of explosion if heated.

Reactions with the following materials may generate heat: Strong acids. Water

Section 3:

Composition/information on ingredients

3.2 Mixtures

Hazardous ingredient:

| Ingredient | EINECS | CAS | Reach number | CLP Classification | Percent |
| --- | --- | --- | --- | --- | --- |
| Alcohol Denat | 603 -002-00-5 | 64-17-5 | 01-2119457610-43-xxxx | H225 H319 | 25 -50% |
| Parfum (fragrance) | N/A | N/A | N/A | H315.H317,.H319, H411 | 1.0 -5.0% |
| PERTROLEUM GASES, LIQUEFIED | 270-704-2 | 68476-85-7 | Exempt | H220; H280 Flammable Gas, Category 1 | 25 -50% |

Section 4:

First aid measures

4.1. Description of first aid measures

Skin contact: Intended use. If irritation should occur, cease using immediately.

Eye contact:   Bathe the eye with running water for about 15 minutes If                                                                                                                                 symptoms persist seek medical advice.

Ingestion: Do not induce vomiting. Wash out mouth with water. Give 1 cup of

water to drink every 10 minutes. If symptoms persist seek medical  advice.

Inhalation: Move to fresh air in case of accidental inhalation of vapours. If symptoms persist seek medical advice.

4.2. Most important symptoms and effects, both acute and delayed

General Information: The severity of the symptoms described will vary dependant on the concentration and length of exposure.

Skin contact: Prolonged contact may cause irritation and redness at the site of contact.

Eye contact: May cause irritation and redness.

Ingestion: No specific symptoms known, but may cause discomfort if swallowed.

Inhalation: In high concentration may cause breathing difficulties.

Delayed/immediate effects: Immediate effects can be expected after short-term exposure.

4.3. Indication of any immediate medical and special attention needed.

None.

Section 5:

Fire-fighting measures

5.1. Extinguishing media.

Extinguishing media: Use water spray to cool containers.

Carbon dioxide.

Dry chemical powder.

5.2. Special hazards arising from the substance or mixture

Exposure hazards: Extremely flammable

5.3. Advice for fire-fighters

Advice for fire-fighters: Wear self-contained breathing apparatus. Wear protective clothing

to prevent contact with skin and eyes. Fight fire remotely due to possible exploding aerosol containers.

Section 6

Accidental release measures

6.1. Personal precaution, protective equipment and emergency procedures.

Personal precaution: Wear protective clothing, gloves eye and face protection. Eliminate all sources of ignition. Evacuate the area immediately.

6.2. Environmental precautions

Environmental precautions: Do not discharge into drains or rivers. Contain the spillage using

bunding.

6.3. Method and material for containment and cleaning up

Clean-up procedures: Absorb into dry earth or sand. Dispose of according to the Local Authority 				Regulations.

6.4. Reference to other sections:       None

Section 7:

Handling and storage

7.1. Precaution for safe handling

Handling requirements: Ensure there is sufficient ventilation of the area. Smoking is

forbidden. Pressurised container: Do not pierce or burn, even after use.

7.2. Conditions for safe storage, including any incompatibilities

Storage conditions: Store in a cool, well ventilated area. Keep away from sources of

Ignition. Keep out of direct sunlight.

Suitable packaging: As supplied aerosol containers

7.3. Specific end use(s):  The identified uses for this product are detailed in section 1.2.

Section 8:

Exposure controls/personal protection

8.1. Control parameters

Hazard ingredients:

Workplace exposure limits:

| Parfum |  |
| --- | --- |
| State | 8 hour TWA | 15 min. STEL |
| UK | 150ppm | 200ppm |

| Alcohol Denat |  |
| --- | --- |
| State | 8 hour TWA | 15 min. STEL |
| UK | 1000ppm/1920mg cum | - |

| PETROLEUM GASES LIQUEFIED |  |
| --- | --- |
| State | 8 hour TWA | 15 min. STEL |
| UK | 1750mg/CuM | 2180mg/CuM |

8.2. Exposure Control

Engineering measures: Ensure there is sufficient ventilation of the area, ensure lighting and

electrical equipment are not a source of ignition. The floor of the storage room must be impermeable to prevent the escape of liquids.

Respiratory protection: Gas/vapour filter, type A: organic Vapours (EN141).

Hand protection:	 Use protective gloves to specification EN1149-5 compliant.

Eye protection: 	Tightly fitting safety goggles

Skin protection:	Protective Clothing.

Environmental:		 Prevent from entering in public sewers or the immediate environment.

Section 9:

Physical and chemical properties

9.1. Physical and chemical properties

| Physical State | Aerosol |
| --- | --- |
| Appearance(Aerosol) | Spray |
| Odour | Characteristic of variant |
| Ph | 5.5 -7.5 |
| Melting Point/Freezing Point | No data available |
| Boiling Point/Range | N/A (Aerosol) |
| Flash Point | -40 o C |
| Evaporation Rate | No data available |
| Flammability (Solid, Gas) | No data available |
| Upper/Lower Flammability | No data available |
| Vapour Pressure | 4.0 bar @20c |
| Specific Gravity | 0.610 – 0.625 |
| Water Solubility | Very soluble |
| Solubility Other Solvents | No data available |
| Partition Coefficient: n-octanol/water | No data available |
| Auto-Ignition Temperature | No data available |
| Viscosity | No data available |
| Explosive Properties | No data available |
| Oxidising Properties | No data available |

9.2. Other information:  No data available

Section 10:

Stability and reactivity

10.1. Reactivity:   Stable under recommended transport or storage conditions.

10.2. Chemical stability:  Stable under normal conditions. Stable at room temperature.

10.3. Possibility of hazardous reaction:  Hazardous reaction will not occur under normal transport or

storage conditions.

10.4. Conditions to avoid: Temperatures exceeding 50 oC. Should not be stored for long periods

above 25 oC.

10.5. Incompatible materials: none known

10.6. Hazardous decomposition products:  In combustion emits fumes of carbon dioxide/carbon

Monoxide.

Section 11

Toxicological information

11.1. Information on toxicological effects

Symptoms/routes of exposure

Skin contact: There may be irritation and redness at the site of contact.

Eye contact: There may be irritation and redness.

Ingestion: There may be soreness and redness of the mouth and throat.

Inhalation: There may be irritation of the throat with a feeling of tightness in the chest.

Delayed/immediate effects: Immediate effects can be expected after short-term exposure.

| Acute Toxicity; | No known effect |
| --- | --- |
| Skin Corrosion/Irritation; | No known effect |
| Serious Eye Damage/Irritation; | No known effect |
| Respiratory Or Skin Sensitisation; | No known effect |
| Germ Cell Mutagenicity; | No known effect |
| Carcinogenicity; | No known effect |
| Reproductive Toxicity; | No known effect |
| STOT-Single Exposure; | No known effect |
| STOT-Repeated Exposure; | No known effect |
| Aspiration Hazard. | No known effect |

12. ECOLOGICAL INFORMATION

Product : The product itself has not been tested.

Toxicity

The ingredients in this formula have been reviewed and no adverse impact to the environment is

expected when used according to label directions

| Toxicity to fish |
| --- |
| Component | CAS | End Point | Species | Value | Exposure Time |
| Alcohol Denat | 64-17-5 | LC50 | Fish | No data avaliable | 96hours |
| Parfum | N/A |  | Very toxic to aquatic life with long lasting effects. | No data avaliable |  |
| Liquefied petroleum gas | 68476-85-7 | LC50 | Physical properties indicate that petroleum gases will rapidly volatilise from the aquatic environment and that acute and chronic effects would not be observed in practice. |

| Toxicity to aquatic invertebrates |
| --- |
| Component | CAS | End Point | Species | Value |
| Alcohol Denat | 64-17-5 | EC50 | Daphnia magna | No data available |
| Parfum | N/A | No data available | No data available | No data available |
| Liquefied petroleum gas | 68476-85-7 | Physical properties indicate that petroleum gases will rapidly volatilise from the aquatic environment and that acute and chronic effects would not be observed in practice |

| Toxicity to aquatic plants |
| --- |
| Component | CAS | End Point | Species | Value | Component |
| Alcohol Denat | 64-17-5 | IC50 | Algae | No data available | No data Available |
| Parfum | N/A | IC50 | Algae | No data available | No data Available |
| Liquefied petroleum gas | 68476-85-7 | No information available. | No information available. | Physical properties indicate that petroleum gases will rapidly volatilise from the aquatic environment and that acute and chronic effects would not be observed in practice |

| Persistence and degradability |
| --- |
| Component | CAS | Biodegradation |
| Alcohol Denat | 64-17-5 | The product is biodegradable. |
| Parfum | N/A | No data available |
| Liquefied petroleum gas | 68476-85-7 | Expected To Be Readily Biodegradable. Oxidises Rapidly By Photo Chemical Reactions In Air. |

| Bio accumulative Potential |
| --- |
| Component | CAS | Bio concentration factor (BCF) | Partition coefficient |
| Alcohol Denat | 64-17-5 | The product is not bioaccumulating |  |
| Parfum | N/A | No data available |
| Liquefied petroleum gas | 68476-85-7 | Not expected to bioaccumulate significantly. |

| Mobility |
| --- |
| Component | CAS | End point |
| Alcohol Denat | 64-17-5 | Soluble in water |
| Parfum | N/A | No data available |
| Liquefied petroleum gas | 68476-85-7 | Because of their extreme volatility, air is the only environmental compartment that hydrocarbon gases will be found. |

| PBT and vPvB assessment |
| --- |
| Component | CAS | Results |
| Alcohol Denat | 64-17-5 | Not aplicable |
| Parfum | N/A | This substance does not meet the PBT/vPvB criteria of REACH, annex XIII. |
| Liquefied petroleum gas | 68476-85-7 | The substance does not fulfil all screening criteria for persistence, bioaccumulation and toxicity and hence is not considered to be PBT or vPvB. |

Other adverse effects:  None known

Section 13:

Disposal considerations

13.1. Waste treatment methods

Disposal operations: Dispose of as per the Local Authority Regulations.

Section 14: Transport information

Classified as dangerous goods for carriage under road/rail/sea/air regulations. This product is packed in accordance with the Limited Quantity Provisions of CDG, ADR and IMDG. These provisions allow transport of aerosols of less than 1 litre packed in cartons of less than 30kg gross weight to be exempt from control providing that they are labelled in accordance with the Limited Quantities requirements of these regulations.

14.1. UN number :	UN1950

14.2. UN proper shipping name:	AEROSOLS

14.3. Transport hazard class(es):	2.2

14.4 Packing group:	None allocated

14.5. Environmental hazards

Environmentally hazards: No                                              Marine pollutant: No

14.6. Special precautions for user:		See section 8 for safe handling

Section 15: Regulatory information

15.1. Safety, health and environmental regulations/legislation specific for the substance or mixture.

EU legislation.

The product is as classified under GHS/CLP- Regulation (EC) No 1272/2008 classification, labelling & packaging of substances & mixtures. Ingredients are listed with classification under GHS/CLP - Regulation (EC) No 1272/2008 classification, labelling & packaging of substances & mixtures.

15.2. Chemical safety assessment:  Safety assessment has been carried out as this is a cosmetic 						product.

Section 16: Other information

Other information: This information is based on our present knowledge. However,

this shall not constitute a guarantee for any specific product

features and shall not establish a legally valid contractual relationship.

Key literature references and sources for data

Material Safety Data Sheet, Miscellaneous manufacturers.

Revision : Original January 2019

SDS status The Hazard Statements listed below in this Section No 16 relate to the Raw Materials (Ingredients) in the Product (as listed in Section 3) and NOT the product itself. For the Hazard Statements relating to this Product see Section 2.

Hazard statements in full :	H220 Extremely flammable gas.

H222 Extremely flammable aerosol

H229 Pressurised container. May burst if heated.

H226 Flammable liquid and vapour

H272 May intensify fire; oxidiser.

H280 Contains gas under pressure; may explode if heated.

H304 May be fatal if swallowed and enters airways.

H301 Toxic if swallowed, in contact with skin or if inhaled

H315 Causes skin irritation.

H317 May cause an allergic skin reaction.

H318 Causes serious eye damage.

H336 May cause drowsiness or dizziness

H361 Suspected of damaging fertility or the unborn child

H319 Causes serious eye irritation.

H400 Very toxic to aquatic life.

H411 Toxic to aquatic life with long lasting effects.

H410 Very toxic to aquatic life with long lasting effects

H290 May be corrosive to metals.

H314 Causes severe skin burns and eye damage.

Abbreviations & Acronyms

ADN European Agreement Concerning the International Carriage of Dangerous Goods by Inland waterways

ADR European Agreement Concerning the International Carriage of Dangerous Goods

By Road

CAS Chemical Abstract Service Number

CDG The Carriage of Dangerous Goods and Use of Transportable Pressure Equipment Regulations

CLP Classification Labelling & Packaging Regulation (EC No. 1272/2008)

COMAH Control of Major Accident Hazards

DSEAR The Dangerous Substances and Explosive Atmospheres Regulations

EH40 Workplace exposure limits -Containing the list of workplace exposure limits for use with the Control of Substances Hazardous to Health Regulations

EINECS European Inventory of Existing Commercial Chemical Substances

EN European Standard

GHS Global Harmonised System of Classification and Labelling of Chemicals

IMDG International Maritime Dangerous Goods Code

OEL Occupational Exposure Limit

PBT Persistent Bio accumulative and Toxic

vPvB Very Persistent and Very Bio accumulative

PPE Personal Protective Equipment

PSSR The Pressure Systems Safety Regulations

REACH Registration, Evaluation, Authorisation and Restriction of Chemicals

RID Regulations Concerning the International Carriage of Dangerous Goods by Rail

RIDDOR Reporting of Injuries, Diseases and Dangerous Occurrences Regulations

STEL Short-Term Exposure Limit

TWA Time-Weighted Averages

WEL Workplace Exposure Limit